The REWOLF project
Stochastic fluctuations of light speed measurement

abstract
In this proposal, we show that by using standard instrumentation we can measure a possible fluctuation of the speed of light predicted by some theories. We also introduce the idea to integrate this apparatus in the Virgo experiment to reach the finest results.

General idea
The objective of the REWOLF project (name?) is to detect a possible group velocity fluctuation of light in vacuum. It is important to note that, even if a limit was put thanks cosmological observations, no dedicated experiment was yet done.
This fluctuation is expected to be stochastic and can be studied with the arrival time of a short light pulse after a propagation in the vacuum. The longer the propagation path, the wider the timing enlargement of a pulse is.
In the first theory family (Th 1), the velocity fluctuations are predicted if the photon propagation is considered as a succession of interactions with pairs of ephemeral (virtual) fermions. This kind of model is developed in (ref) and (ref). More generally, from such definition of the vacuum filled with virtual fermions, one can demonstrate that the values of μ0 and ε0 and the group speed of light appear naturally at the correct scale. More over, the equation c_group = sqrt(1/mu0e0) can be deduced independently from the Maxwell equations.
This description of the vacuum predicts fluctuations of the photons transit time of the order of σt ≈ 50 [as] * sqrt(L[m]) (attosecond, 10^-15 s) at the distance L. The experimental signature of such an effect is an enlargement of the light pulse temporal envelop during its propagation. This enlargement increase proportionally to the square root of the path length in the vacuum.
There are two things to note for the model (ref). First, the fluctuations depends on the inverse of the square root of the total pair energy. This order of magnitude of 50 as is given for a peaked energy distribution. Since no final interpretation is given to this energy distribution, its average can be bigger (with weak effect on the fluctuations order of magnitude), or smaller (a non relativistic level of energy bring the fluctuation FWHM at σt ≈ 100 [as] * sqrt(L[m])).
In this model, this phenomenon is totally independent from the light wavelength and the phase as it relies only on a photon interaction probability with the ephemeral pairs.

In the second family of theory (Th 2), Have to write that there are other linear dependent theory (we are looking for references)

The current limit put on this fluctuation effect is σt ≈ 200 as m^-1/2 (Cosmology observation (ref)). The purpose of this project is to push this limit up to the theoretical predictions, and, possibiy, to distinguish the various theoretical fluctuations predictions.
In the case of 100 m light path and 2 fs detector resolution the current cosmological limit can be reached in laboratories.
The final goal of this experiment is to use ultrashort pulses of 5 fs FWHM and a path of 6 km. According to the predictions of the model 1, the time width of the pulse is expected to be spreaded to 7 fs. It is possible to see this enlargement using detectors with a resolution of about 2 fs.
The best method to characterize both the initial and final pulse must be an intensity auto-correlation system(ref).

We will see in the next parts a description of the different phases of the experiment and the chosen technical solutions.

Experimental setup description.

The setup has three main components: the light sources, the propagation path and the detector. We plain several phases of the experiment:
Phase-0) Laboratory tests of the source and the detector. At this phase we verify the source properties and accuracy of the detector.
Phase-1) Laboratory measurements with a multi-reflections cell (Herriott cell (ref)). In this phase we plan to reach the current cosmological limit of the light transit time fluctuations. The light path should reach the 100 m scale. It was calculated that an accurate measurement can overtake this limit by about 30%.
Phase-2) Using the know out of the phase-0 and phase-1 (source, mirrors and detector), the final experimental setup with km-scale path. Here we plan to reach the model limit for the light transit dispersion. There are two possibilities - an improved Herriot cell [ref], or to integrate the setup with the VIRGO [ref] facilities.

In the further sections the technical solutions of the experiment components will be described.

Laser choice
According to a research for a good candidate for the laser choice, the characterstics are
fa con punti
There are several commercial options for the femtosecond light sources. Titanium-Sapphire lasers are able to produce pulses with a width below 10 fs. Their typical frequency is ~80 MHz and the energy is 2-6 nJ per pulse. The wavelength has a range of about 700-1000 nm. The divergence is < 2 mrad and the beam diameter is < 2.5 mm. For the pulse measurement an energy of several nJ may not be enough. In this case an amplification should be used. Ti:Sapphire multipass amplifier with the dispersion compensation is able to provide <25 fs pulses with energy of ~1 mJ. Stretching of this pulses is possible to <7 fs with hollow fiber compressors. For the commercial solutions, please refer to www.femtolasers.com (Rainbow oscillator + CEP Pro amplificator + Kaleidoscope compressor) or www.thorlabs.de (Octavius-85 laser).

Light path

Considering the phase-1 of the proposal we need a meter scale of Herriot cell with about 100 reflections on mirrors. To ensure < 2/3 energy loss at the end of the path >0.99 reflectivity coefficient is required. This requirement is possible with gold mirrors with a roughness of less than 100 Å (ref). This kind of mirrors are commercially available. The time dispersion due to thermal fluctuations of the mirrors are negligible comparing to the dispersion due to the mirror roughness.

The air group velocity dispersion is at the order of 1 fs^2/m (at 1 atm) (ref Group-velocity-dispersion measurements of atmospheric and combustion-related gases using an ultrabroadband-laser source) Which represents, for a pulse of 5 fs width, a dispersion of 0.2 fs/m. This dispersion is directly proportional to the pressure. That means that to reach a negligible total dispersion (less than 10 as), the pressure should be less that 0.5 mbar for the 100 m scale experiment, and less than 0.05 mbar for the km scale. These order of magnitude are quite easy to reach in the both cases.

According to the experience from the phase-1, the extension to the phase-2 straight forward. Due to the length of several kilometers, 0.1 μrad divergence of the light source is needed to keep cm scale beam radius. This will need an addition optics collimator
Note that in the case of the integration in the Virgo experiment, the pressure inside the detector is 10^-11 mbar, which is far better that the requirements.

Detector
For this experiment a direct spectrometry or phase measurement methods cannot be used because they rely on some assumption on the pulse properties and use the Fourier limit to deduce its shape.
As an alternative there are several kinds of autocorrelator detectors, and FROG (Frequency Resolved Optical Gating) which satisfy the requirements.
In general the measure is done by splitting the pulse beam in two parts and sending them on a non-linear crystal. The crystal, thanks to the second or third harmonic generation effect, will produce an output beam proportional to the cumulative intensity of the input beams. By adding a delay to one of the incoming beam (changing one path length), it becomes possible to measure the full autocorrelation of the incoming pulse.

By using a surface third harmonic generation FROG it is possible to characterize pulses with ~5 fs width and an intensity of few nJ (ref). The time resolution of such a system can reach the sub fs order of magnitude.

Perspectives
The goal for the precision of the measurement is about 1 fs, the measurement at 6 km can exclude no fluctuation hypothesis at 3 sigma, assuming the 50 as/m1/2 fluctuation. The additional measurement at 12 km can exclude no fluctuation hypothesis at 5 sigma.
To exclude the linear dependance of the fluctuations with distance, expected in some alternative models (although at smaller scale) 18 km measurement (equivalent to 3 round trip in the Virgo tunnel) is enough to reach 5 sigma difference.